## Slide 1: Programming Platform for Internet of Things (IoTs) Applications

## Slide 2: Micro-Controller Platform
Micro-Controller Unit (MCU) contains RAM, ROM and IO
Micro-Processor Unit (MPU) only contains the CPU
System on Chip (SoC) refers to MCUs with a greater number of onboard peripherals and functionality
http://www.microchip.com
http://www.ti.com
http://theairboard.cc

## Slide 3: C Language: Header and C++ Files
#ifndef __LED_H_
#define __LED_H_
#include <system_lib.h>
#include “user_lib.h”
#include “UserFolder/lib.h”
extern int T_on;
extern int T_off;
void setOn(long duration);
void setoff(long duration);
#endif
#include “led.h”
int T_on;
int T_off;
int counter;
void setOn(long duration){
//TODO: set LED on here
}
void setoff(long duration){
//TODO: set LED off here
}
void delay(long duration){
//TODO: set delay here
}

## Slide 4: C Language: Main File
#include “led.h”
#include “timer.h”
#include “gpio.h”
#include “button.h”
void main(){
initGPIO();
initTimer();
initButton();
initLED();
….
….
while(1){};
}
void timer_isr(){
}
void ext_isr(){
}
LED
TIMER
GPIO
BUTTON
System operations are implemented in interrupt functions
Modules/ Libraries are included
Modules/ Libraries are initiated

## Slide 5: Finite State Machine (FSM)
Finite-State Machine (FSM) or Deterministic Finite Automata (DFA), finite automaton, or simply a state machine, is a mathematical model of computation
A turnstile
Current State | Input | Next State
Locked | Coin | Unlocked
 | Push | Locked
Unlocked | Coin | Unlocked
 | Push | Locked

## Slide 6: Finite State Machine Programming
while(1){
  switch(status){
    case LOCKED: lock_turnstile(); //operation in a state
    if(Coin == true) //transition condition
    status = UNLOCKED; //next state
    break;
    case UNLOCKED:
    unlock_turnstile(); //operation in a state
    if(Push == true) //transition condition
    status = LOCKED; //next state
    break;
    default:
    break;
    }
}

## Slide 7: Example 1
Given an LED turns on for T_on and then turns off for T_off.
  Design an DFA for this LED
  Implement the DFA in Arduino
digitalWrite(13, HIGH): turn on the LED
digitalWrite(13, LOW): turn off the LED
setTime(duration): set a clock (timer_flag = 0), when the clock is expired, timer_flag = 1; duration is in mili-seconds.

## Slide 8: Answer
INIT: Set pin 13 to OUTPUT mode, set timer
LED_ON: Turn on the LED
LED_OFF: Turn off the LED
INIT
LED_ON
LED_OFF
timer_flag == 1
timer_flag == 1

## Slide 9: Answer (Arduino Code)
void loop(){
  switch(status){
    case INIT: pinMode(13, OUTPUT);
    setTimer(T_on);
    status = LED_ON;
    digitalWrite(13, HIGH);
    break;
    case LED_ON:
    if(timer_flag == 1){
  status = LED_OFF;
  setTimer(T_off);
  digitalWrite(13, LOW);
    }
    break;
    case LED_OFF:
    if(timer_flag == 1){
  status = LED_ON;
  setTimer(T_on);
  digitalWrite(13, HIGH);
    }
    break;
    default:
    break;
    }
delay(10);
}
void timer_run(){
if(timer_counter > 0)
timer_counter--;
if(counter_timer == 0)
timer_flag =1;
}
void setTimer(long duration){
timer_counter = duration;
timer_flag = 0;
}

## Slide 10: Example 2
Design a smart lock which accepts 4 digits as a secrete code. However, there is a time-out for each digit (e.g. T_out = 5s). After this period, the system is reset

## Slide 11: Embedded Platform based on Operating System
Embedded means something that is attached to another thing.
“Any sort of device which includes a programmable computer but itself is not intended to be a general-purpose computer” [Marilyn Wolf]
Embedded system has three components:
  Hardware
  Real Time Operating System (RTOS)
  Software

## Slide 12: Classification of Embedded System
Small Scale
Medium Scale
Sophisticated Scale

## Slide 13: Processor
Processor is the heart of the Embedded Syste
General Purpose processor (GPP)
  Microprocessor
  Microcontroller
  Embedded Processor
  Digital Signal Processor
Application Specific System Processor (ASSP)
Multi Processor System using GPPs

## Slide 14: Operating System: Linux and Android
Connectivity and UI
  Two powerful operating systems used in most of the embedded systems
  Wireless connectivity and graphics interface: Android OS
  Linux comes with a complex flow and it might be difficult for a beginner to understand it
Power management
  Android and Linux supports effective power management compared to real time operating systems
Responsiveness
Cost

## Slide 15: Android Operating System Component

## Slide 16: Android Boot File
mkdir /system
mkdir /data 0771 system system
mkdir /cache 0770 system cache
mkdir /config 0500 root root
mkdir /metadata 0770 root root
service yunos_preinstall /system/bin/yunos_preinstall.sh
user root
group root
class main
disabled
oneshot

## Slide 17: Android Resource File
IR Remote Data

## Slide 18: Android System File
System apps
User apps
Launcher apps
Preinstall apps
Libs
KeyLayout
…

## Slide 19: Lab 2: LED Blinky on Android Things
Hardware connection

## Slide 20: Create an Android Things Project
dependencies { ... compileOnly 'com.google.android.things:androidthings:+' }

## Slide 21: Add permission in Android Manifest
<uses-permission android:name="com.google.android.things.permission.
USE_PERIPHERAL_IO" />

## Slide 22: MainActivity.java
Step 1: Declare a pin name wired to LED
  private static final String LED_PIN_NAME = "BCM26";
Step 2: Implement initGPIO function
Step 3: Call initGPIO() on OnCreate()

## Slide 23: MainActivity.java
Step 4: Release the pin when the app is closed

## Slide 24: MainActivity.java
Step 5: Create a Timer
Step 6: Call this function on OnCreate()

## Slide 25: Exercise
Implement a Light Traffic System